## Slide 1: Why OT Cybersecurity Engineers Drink So Much
A look into the Operational Technology environment, how IR is performed there and the evolution of it in the Project Obsidian challenge.

## Slide 2: CYA Statement
My statements are my own and do not reflect the thoughts feelings or beliefs of my employers (past or present) or any other organization that I had/have connections with.
All pictures that are included which were not generated by me (which includes a link to the source where I pulled it from) are the intellectual property of the owner/creator and not mine.
Additional notes are available in the presentation slides

## Slide 3: Agenda
Who we are
An overview of OT
  IT/OT differences, similarities and convergence
  Tech stack – a modern manufacturing plant as a museum of old tech
  Threat landscape
  Black hat / Red team point of view
  White hat / Blue team point of view
Why & how did we build this for the Obsidian Project
IR in the OT environment
Notes: This is going to cover a lot of material. By the end of it I am hoping that you will have a grasp of a few specific things:
Overview of the OT environment, it’s challenges and how we can integrate our knowledge and skills of IT security to improve the safety of manufacturing
What, why and how we implemented this into the Project Obsidian challenge
Have an introductory understanding of how to build up the IR capabilities of your teams to support investigations and security in the OT environment

## Slide 4: Who we are – Project Obsidian OT Team
Jason (ThatDeadGuy) – OT Team Lead
Education
  BS Electronics Engineering Technology: Texas A&M University
  MBA with a Project Management Focus: Capella University
Relevant Certifications
  IEC 62443 Expert
  GRID – GIAC Response and Industrial Defense
Experience:
  3 yrs Controls Engineer: Automotive parts manufacturing
  10 yrs Software Controls Engineer: O&G rig manufacturer
  5 yrs as an OT/ICS cybersecurity engineer focused on
    Secure product development
    OT risk evaluation & compliance assessment
    OT architecture review, design and upgrade
    OT and enterprise incident response

## Slide 5: Who we are – Project Obsidian OT Team
Lex – OT Team Member
Education
  BS Computer Engineering: Virginia Tech University
Experience:
  2yrs Cybersecurity analyst in Oil & Gas exploration rig manufacturing
Primary Obsidian Focus
  Keeping the rest of us on track
  Researching deployment options that were open source able
  Modbus communications implementation for remote IO simulation

## Slide 6: Who we are – Project Obsidian OT Team
101% Pure Fool – OT Team Member
Education
  BS Electrical Engineering: Texas A&M University
Experience:
  2yrs Cybersecurity analyst in Oil & Gas exploration rig manufacturing
Primary Obsidian Focus
  Breaking what has been implemented during “testing”
  Researching malware options that is realistic to find in the OT environment
“A lot is done and a lot less is accomplished”

## Slide 7: Overview of OT – What is OT
OT is focused on supporting and controlling physical devices to manage a process that generates a specific environment or product.
Industrial Control Systems (ICS) are systems that are used to control the specific process.
OT encompasses those ICS systems as well as other systems that support the manufacturing process such as bar code readers & printers, thermal cameras for vision systems and x-ray machines that perform quality checks on the product

## Slide 8: Overview of OT – What is OT
IT
OT
ICS
SCADA
PLC
IT: Information Technology
OT: Operational Technology
ICS: Industrial Control System
SCADA: Supervisory Control and Data Acquisition
PLC: Programmable Logic Controller
Notes: IT Examples: Active Directory; Exchange servers, File & Print Servers; SAP and business focused traditional IT endpoints
OT Examples: Bar code readers & printers, X-ray machines for quality checks, production reporting servers, time clocks, fire enunciation systems (cell alerts & paging)
ICS Examples: ABB Pick & Place robot, industrial bakery oven, ammonia chiller/refrigeration system, stamped metal heat treating furnace
SCADA Examples: Power generation and grid balancing; waste water treatment management and monitoring; chemical refining facilities
PLC Example: Drive control for a conveyor at an airport, sensor monitoring and chemical adding for a water treatment system

## Slide 9: Overview of OT: IT/OT Comparison
IT
Priorities: CIA Triangle
Replace Equipment: 3-5 yrs
View of cybersecurity:
Necessary Evil
Architecture:
Segmentation, IAM,
Logging & Tools
Skills & Knowledge:
Well established
education options
OT
Priorities: Safety, availability
Replace Equipment: 15-20+ yrs
View of cybersecurity:
Stay away, they break stuff
Architecture:
Limited Segmentation,
Few if any tools
Skills & Knowledge:
Tribal; Technology, Process and safety focused
Notes: IT vs OT - How is it actually different
Priorities
  IT: CIA
  OT: SAIC (Safety then availability to run product, integrity only matters for quality and reporting requirements, don't care that much about confidentiality)
Timelines
  IT: 5 years to replace equipment
  OT: 20 years to replace MOST equipment
c) Skill Sets & Knowledge
  IT: Well established ways to train, test and validate a person's capability to perform functions; security knowledge is baked into a lot of different paths within IT
  OT: Much more tribal as it relies not only on technology stacks but also process and safety knowledge; security knowledge is missing from most training pipelines
Acceptance of cybersecurity
  IT: necessary evil
  OT: it breaks things and we don't believe we are a target
Architecture
  IT: Segmentation, IAM, logging and other tools are common
  OT: Flat networks with limited, if any, segmentation; equipment doesn't necessarily support a full TCP/IP stack much less logging and reporting; Need to get a lot of down time to implement architecture changes
Risk Calculations
  IT: Likely to take something down to clean it up and/or fix the vulnerability
  OT: Might leave something infected on the network for months until there is down time to clean it unless it is affecting safety/availability; vulnerabilities may never be fixed depending on where the equipment is in the network and the likely level of exposure

## Slide 10: Overview of OT: IT/OT Comparison
https://securityboulevard[.]com/2020/11/too-late/
Many things are considered when designing a process
Safety
Environmental requirements
Certification requirements
Power consumption
Metrics collection

## Slide 11: Overview of OT: Tech Stack - Equipment
High cost for the equipment due to environmental requirements and restrictions; so the break even point of the equipment may take years to achieve
Equipment is often specialized/customized for the process
Federal certifications may be required (FDA, EPA, FCC)
Upgrades can affect certification whereas a direct replacement won’t
Limited vendors/integrators may restrict what options you have for an OS and for security measures
Patches can have significant negative impacts on the process
Notes: A $23,000 Human Machine Interface (HMI), which is the touch screen used to control a process is not uncommon. Special environmental requirements such as needing to operate in 120°, no/limited mechanical parts due to high vibration often drive up the costs substantially.
Depending on the environment Federal certifications may apply. I have seen these in regards to medical, food inspection and critical safety process equipment. The challenge this presents is that the whole configuration will have to be recertified if a patch is applied. This often takes a long time and requires the equipment to not be in production until the verification and recertification is completed.
Due to the federal certifications a limited number of vendors and integrators are available to perform this work. In one recent case I was dealing with there are only two companies in the US that can provide these certified systems. So trying to push them to improve security is challenging as you cannot simply find someone else to do the work.
Storytime: Patching in the OT environment is risky. When Wannacry hit some of the patches effectively, and rightfully turned off, SMBv1. While this didn’t significantly impact the IT operations for some areas of the OT environment this brought things to a dead stop. Some of the equipment was running on Windows NT, 2000 and XP. These systems were maintained because they directly supported critical equipment for the process control and the vendor had either gone out of business or was simply charging too much to upgrade the system when it was still working just fine. Turning off SMBv1 however shut down how they were doing background data transfers and prevented the equipment from knowing what to make next. Ultimately SMBv2 and 3 were implemented across most of the network, but jump hosts for the background transfer were built to allow SMBv1 to run to certain machines that couldn’t be upgraded and the rest of the network on the updated versions.
Having to hold onto old equipment is more of the norm than anything and can result in interesting issues such as people buying old replacement equipment off ebay.

## Slide 12: Overview of OT: Tech Stack - Access
Some environments have an Active Directory
  Might be manufacturing only
  Might be connected to the enterprise
A lot of environments have local access credentials for daily operations and AD access for servers
  Local access creds rarely rotate, are commonly shared and often written down somewhere at the station
https://chameleonmemes[.]com/tag/password-meme/
Notes: b) Identity and access management
1) Ideal
a) Domain connected and controlled
b) user specific credentials with rotation and complexity
c) Logging of security events
2) Real
a) Local accounts
b) Shared names and credentials
c) No logging capabilities or configurations completed

## Slide 13: Overview of OT: Tech Stack - Network
Not all OT devices belong on a network
Some devices support limited protocols
  Limited protocols do not include the full TCP/IP stack or function calls
  Some protocol implementations do not support encryption, authentication or proper error handling when faced with those requests
Most OT networks were designed without segmentation so support activities and monitoring could happen from anywhere
Modified versions of the Purdue model are improving the architecture
https://www.automatedelectrics[.]com.au/plc5-migration-solutions.html
Notes: The networks were not originally designed to be connected to the enterprise however a desire for real time data has pushed these areas to be connected. The OT network is significantly less dynamic than the IT, but it also has older equipment that has been customized to focus on speed of control instead of networking protocol support.
The picture shows the upgrade from an older PLC5 to an Allen-Bradley Logix system. This upgrade probably cost $100,000-$150,000. Alternatively some sites, that still have older hardware available will opt to put a protocol converter in front of the PLC5 and convert TCP/IP over to a serial protocol that the PLC5 supports. This option will cost them $500-$2,000.
a) Network architecture
1) Ideal
a) Accurately Documented
b) Segmentation
c) Standardized remote access with visibility
d) Standard security tools
2) Real
a) What documentation exists is an excel spread sheet that should be about 85% correct hopefully; not all equipment is listed, some might have never been reported to the facility during installation (remote access & support)
b) Might be a firewall at the border between IT & OT because both sides were tired of IT scans causing problems; other than that limited segmentation via VLANs w/o ACL
c) The network gets bridged by cellular hot spots and modems whenever remote support is needed
d) No/limited logging; AV/EDR is almost non-existant (may impact availability of controls)

## Slide 14: Overview of OT: Tech Stack – Security Tools
Technology Asset Management (TAM) / Inventory
  Provides context for what is normally there and what it does
Passive Network Anomaly Detection
  Monitor the network for known bad patterns
  Identifies new/odd connections that should be reviewed
End Point Detection and Response (EDR)
  Enables detection of malicious activities and permits response
Anti-Virus
Application Allowlisting
Integrated Logging
Notes: TAM: Use an OT specific solution not all equipment supports SNMP, WINRM or full SSH. Look for a solution that can address not only IP layer devices, but one that supports CIP, S7, Data Highway+ and other serial protocols
Network Detection: Often requires a fair amount of additional networking to support span ports, one of the least invasive ways to monitor the OT environment for malicious activities
EDR: Can be typically placed on servers, however lower level devices such as windows based PLCs and HMIs it is often not done. This is because of the risk of it consuming too much memory or processor during critical control actions on the equipment. This can result in a safety risk.
AV: Same as EDR
Application Allowlisting: Often a good solution when EDR & AV are not available for a device. It provides protection while also being tuned to permit normal software packages on that system
Integrated logging: is often easily done at the server level but as you progress to the lower devices such as PLCs and HMIs it is not always feasible. The device may not have the capacity to forward the logs, or in some cases it may not even collect logs at all.
c) Security tooling
1) Ideal
a) Network Security monitoring
b) log forwarding
c) Asset identification & management
d) AV/EDR on OS based equipment
e) Application allow listing
2) Real
a) Very few companies apply those solutions to the OT environment unless required to

## Slide 15: Overview of OT: What They Do Well
Safety Design
Process safeties are designed in
Disaster Recovery
When equipment needs to run 363 days a year, swapping out and recovering equipment is a must
MacGyver It
Sometimes you don’t have the time or resources to fix things
https://www.inspireuplift[.]com/If-You-Can-T-Fix-It-Macgyver-It-Shirt-Svg-/iu/264618

## Slide 16: Overview of OT: Threat Landscape
How well known is the threat landscape?
  Unfortunately, not very well. Reporting is not required of all critical sectors.
  Differentiating between an attack against the IT infrastructure and the OT environment is rarely released
Is the government after me?
  Depending on who you are, yes.
Are Nation States the primary risk in most of OT?
  No, malware, ransomware and insider threats tend to be the most common threats to OT environments
Notes: Gov’t after me? Certain sectors tend to generate a lot more probes and attacks against the OT environment. These include power generation, water treatment and military production.
Malware that targets OT devices is increasing. Over the last several years we have seen things such as Stuxnet, DarkEnergy2, CrashOverride, Trisis, Industroyer and Pipedream to name a few. Pipedream is one of the latest that appears to be modular and potentially intended to support further development by users within that space.
Why aren’t Nation States the primary risk in OT security? Most companies are looking to make a profit, as such they are more concerned about product and market share. While some segments of the critical infrastructure are significantly more targeted by Nation States most of the manufacturing and operations are outside of these industries. Military components, chemical & oil refining, power generation & distribution and water treatment a high value targets for a Nation State to have access to for when they want to cause damage. However some Nation States are interested in IP theft more than damage.
Cyber criminal organizations are looking for profit and are willing to take anyone that they can hit. Their potential target pool is larger but also more focused on the IT side of the house currently.
Story time: Sofail. A firewall that was deployed on a significant number of drilling rigs ended up having a vulnerability that allowed for the attacker to force it to call back to a listening server. The attackers then remounted the memory that the embedded linux OS was running on and modified several things such as where to get updates from, adding persistence and enabling their C2 to scan and push data through the network. This resulted in malware being pushed to several machines (which most were fortunately patched). Ultimately The firewalls were restored and the affected servers were taken offline. The hard drives were removed and new ones were put in and imaged with a recent backup. Minimal impact was experienced by the rigs. If it had been a Nation State then they would have done significantly more data exfiltration to understand what safeties were in place, what the PLC code was doing and protecting and how it could be bypassed. These activities would have taken a while to perform, but would have allowed them to perform a significant attack.
d) Threat Landscape
0) Objectives
a) Research for a more targeted attack (what PLCs, HMIs, OSes exist)
b) Intellectual Property Theft
c) Force quality issues (Early Stuxnet versions)
d) Force downtime (ransomware; Wannacry)
1) Ideal
a) Limited to Nation States and advanced cyber criminals
2) Real
a) Everything from the last 20 years is still a threat because we don't deploy AV/EDR to a deep level (Nimda & Conficker)
b) reference CISA: information is not fully accurate. limited segments are mandated to report incidents, most are voluntary

## Slide 17: Overview of OT: Black Hat / Red Team POV
Targets
Servers – Historians, Backups, Logistics, Engineering
  Engineering server: PLC/HMI code backups, electrical/mechanical drawings, hardware lists, software inventories
Human Machine Interfaces (HMIs)
  Screen shots, alarm history, process understanding, process access
PLCs / Controllers and IO (Input Output control)
  What can be forced/turned on/off
  What can be changed to alter the production information
Other network connections
  Engineering laptops / workstations
  Enterprise
Notes: Memory only malware is useful in the OT environment because of the reduced frequency with which reboots are done on the systems

## Slide 18: Overview of OT: White Hat / Blue Team POV
Cons
Limited tools deployed
Limited integration of logs
Limited visibility of assets
Limited decision authority
Have to work with Controls Engineers
Pros
Fairly static environment
Gives you a solid reason to drink
https://img.memegenerator[.]net/instances/600x600/72104414.jpg

## Slide 19: Obsidian Project OT Environment: Why
Educational benefit: OT is built on a lot of IT technology, but it generally needs to be handled with kid gloves. This scenario can give some access to that environment without risking personnel or high value equipment
Open Source: By making the project open source we enable people to not only play with some of these tools but to explore how they might be able to protect them without negative consequences
Product selection: While it would have been nice to have a set of simulated Allen-Bradly or Siemens PLCs selecting an open source option allows anyone to use them with out cost
Notes: OpenPLC was selected as it conforms to the standard PLC programming languages and support structures. It is also deployable as a docker image, installed on linux or run on Raspberry Pi hardware.
ScadaBR was selected as an open an available HMI design interface that uses the standard Modbus communication port 502. OpcUA was a desired option, but wasn’t located as a free option during our initial research

## Slide 20: Obsidian Project OT Environment: How
SecEng made the magic happen for deployment and access
Architecture
  An older style network was selected to go with the simpler exploration / work over rig
  The flat network with limited access points is similar to real world applications
  Limited security tools within the environment also mimicked reality
Access
  Shared access account and default credentials being left in place is not uncommon
  Having a spread sheet with network and account details is very common

## Slide 21: IR in the OT Environment: Objectives
IT IR Objectives:
Contain the incident - Reduce risk to other systems
Collect & analyze evidence as quickly as possible
Return systems to operation as quickly as possible
OT IR Objectives:
Get the process to a safe state
Contain the incident - Reduce risk to other systems
Collect & analyze evidence as quickly as possible
Return systems to operation (prioritized order)
Clean up of the systems may not be a priority

## Slide 22: IR in the OT Environment: Foundations
TAM / Inventory: Know normal to find evil
Understand what is critical: What processes matter
Preposition local tools:
  What image & memory collection systems are supported
  What scripts need to be developed to support investigations on older systems without EDR
Preposition remote access when available
Know who to contact and how to work with them
  IT site leads, Controls Engineers, Plant Technical Managers
  Predefine who has decision authority (Can IR order a line to be shut down?)
  Table top the process when possible
How and When should OT contact IR
Notes: 5) Foundational requirements for IR in OT
Understand dependencies internal to the process and external to the organization (Colonial Pipeline)
If product intake is shut down, how long can they operate
If the logistics server in the enterprise area is ransomed, does the facility shut down?
Are there any gov't required logging & reporting expectations
Define & pre-stage tools
Tools for getting images, memory, logs, etc
custom scripts may be needed; these have to be developed based on the systems in the environment; powershell isn't everywhere and PS 2 isn't as capable as PS 5
Define an incident access plan (if we cut the internet to a facility, are we going to wait to get someone on site to deal with it, or are we going to open up some remote support connections)
Who can make certain decisions
RACI - Responsible Accountable Consulted Informed
Isolate the plant from the enterprise network
stop production within the plant
How & When should a location reach out to IR; what information needs to be shared
Define Roles
Incident Director/Commander - communicates with leadership & risk teams
Lead Responder - Guides and directs activities for the investigation; main technical lead for the incident
Evidence & Incident Handlers - acquire and analyze evidence as directed
Archivist - Project Manager for the incident (creates task lists, timeline entries for actions taken, documents findings)

## Slide 23: IR in the OT Environment: Perform IR in OT
Leverage the different teams available
Focus on the major questions
  What is the scope
  Does it affect safety
  Does it pose a risk to production / enterprise
Prioritize certain systems for evidence collection
Order of volatility for forensics
How should the facility recover
Fix the root cause
Hold a retrospective
Notes: 6) Working an Incident in OT
1) Leverage IR, networking and controls engineers to understand the impact to processes; focus on major questions, timely analysis & advisement for moving forward
2) Determine scale of the incident (malware vs remote access)
a) Technical Asset Management (provide context on IP addresses)
b) Network Security Monitoring (visualize & hunt external and abnormal connections)
c) Baseline equipment & IoCs (OT software is different and not what we stare at daily; having a snapshot of a known good clean state gives us a way to compare processes, registeries, connections, etc)
3) Does it affect safety
4) Does it pose a risk to production
a) Can this spread to other processes or to the enterprise side
5) Systems to prioritize for evidence collection (Generally in this order but adjustable based on the situation)
a) Engineering Work Stations
b) Servers (historians, visualization, backup, etc)
c) HMIs
d) PLCs, remote IO & other embedded level devices
6) How do we collect evidence (Order of volatility & value for FORENSICS)
a) Running memory collection
b) Cache & Register data
c) Network status (ARP, routing tables, connections)
d) System Processes
e) Temp Files
f) Hard drive image
7) How can the facility proceed with recovery activities (Make sure you have collected everything you need for forensics)
a) Recovery actions are generally well handled in the OT side of things; IT recovery can get substantially more murky for the local teams
8) Post fire
a) Identify & Fix root cause
b) After action review / post mortum/ retrospective / never let a good incident go to waste

## Slide 24: IR in the OT Environment: Order of Volatility
Running memory
  Memory only malware is effective in OT due to the continuous uptime
Cache & registry data
Network Status (ARP, routing table, connections)
System processes
Temp files
Hard drive image
Different tools and scripts may be needed for different systems due to their age and support capability
Pretesting is highly recommended
Notes: 6) Working an Incident in OT
1) Leverage IR, networking and controls engineers to understand the impact to processes; focus on major questions, timely analysis & advisement for moving forward
2) Determine scale of the incident (malware vs remote access)
a) Technical Asset Management (provide context on IP addresses)
b) Network Security Monitoring (visualize & hunt external and abnormal connections)
c) Baseline equipment & IoCs (OT software is different and not what we stare at daily; having a snapshot of a known good clean state gives us a way to compare processes, registeries, connections, etc)
3) Does it affect safety
4) Does it pose a risk to production
a) Can this spread to other processes or to the enterprise side
5) Systems to prioritize for evidence collection (Generally in this order but adjustable based on the situation)
a) Engineering Work Stations
b) Servers (historians, visualization, backup, etc)
c) HMIs
d) PLCs, remote IO & other embedded level devices
6) How do we collect evidence (Order of volatility & value for FORENSICS)
a) Running memory collection
b) Cache & Register data
c) Network status (ARP, routing tables, connections)
d) System Processes
e) Temp Files
f) Hard drive image
7) How can the facility proceed with recovery activities (Make sure you have collected everything you need for forensics)
a) Recovery actions are generally well handled in the OT side of things; IT recovery can get substantially more murky for the local teams
8) Post fire
a) Identify & Fix root cause
b) After action review / post mortum/ retrospective / never let a good incident go to waste

## Slide 25: Special Thanks
Project Obsidian Security Engineering Team
Without them this portion of Project Obsidian would never have been possible
Their abilities to execute the requests and support a recovering Controls Engineer are impressive to say the least.
Project Obsidian Leadership Team
This has been a great opportunity to show the cross overs in the real world for environments that require kid gloves and to hopefully encourage people to develop the skills needed to support these critical areas.